## Slide 1: NextRoom
Nicolò Palmiero
Luigi Sigillo
Supervisor: Joy Abi Rizk
Repository
https://github.com/LuigiSigillo/IotBigProject

## Slide 2: Changes from 1° delivery
The main changes from the first delivery are:
We faced the problem of the COVID-19 and limited accesses to the museum in our system and redefined our solution taking into account this factor.
After some tests we decided to discard the option to implement the communication between each board and Azure IoT Hub using LoRaWAN. The test we have done to make this decision will be later described.
Since we have the possibility to test on a physical board we have changed our plans to evaluate our system. Indeed now we can do better evaluation tests, and discarded the possibility to use Fit IoT Lab mobile robots.

## Slide 3: The problems
  Personalized tours in the museum
  Museum visits during the COVID-19 emergency

## Slide 4: Our solution for personalized tours
Web application that runs on a smartphone
During a tour suggests the next section you could visit based on the time you have spent in the previous sections
The application will display a preview of the suggested section
  The user could choose to follow it or to jump to another suggestion.
The suggestions are sent every time a user is leaving a section

## Slide 5: Our solution to avoid gatherings
Solve the crowd problem of our personalized tour in these times in which sections cannot be overcrowded:
Dashboard for the curators of the museum to monitor the number of people in the different sections of the museum.
Added features to try to equalize the number of people in each section.
  Suggest the most interesting section for the visitor and, at the same time, try to avoid the formation of gatherings

## Slide 6: A Possible Scenario

## Slide 7: A Possible Scenario

## Slide 8: A Possible Scenario

## Slide 9: A Possible Scenario

## Slide 10: Architecture

## Slide 11: B-L475E-IOT01A Discovery kit
Ultra-low-power STM32L4 Series MCUs based on Arm® Cortex®-M4 core with 1 Mbyte of Flash memory and 128 Kbytes of SRAM
Bluetooth® V4.1 module (BLE technology)
802.11 b/g/n compliant Wi-Fi® module from Inventek

## Slide 12: Typical scenario
BLE technology
Bluetooth beacon functionality

## Slide 13: MQTT Protocol
MQTT protocol
Eclipse Mosquitto MQTT Broker

## Slide 14: Cloud Services
Azure Cloud services
  Azure Function
  Azure IoT Hub
  Azure SQL DB

## Slide 15: The complete flow
Azure App service will host the Web Application

## Slide 16: Technical work done so far
Our work, from a technical point of view up to now is:
We have implemented the cloud infrastructure to make the system work:
  An SQL database with all the necessary tables to maintain useful data to be processed by our system.
  We implemented a scoring algorithm that takes into account the similarity between recent visits and the current visit, and the number of people that is currently in each section.
We have a starting version of the web application that gives suggestion about the next room to visit, taking into account the taste of the visitor and the crowding situation in each section.

## Slide 17: Technical work for the last delivery
The boards in our future plans have to communicate to reach a consensus about the final list of devices in each section, moreover they have to send this list to the cloud.
We do not know if the board can handle this load. Otherwise the computation will be done using the computational power of the cloud as we do now.
The curators dashboard

## Slide 18: Evaluation

## Slide 19: Technical Evaluation
  LoRaWAN and TTN not used anymore.
    60% of message loss with TTN.
  MQTT with Eclipse Mosquitto broker

## Slide 20: Pricing Evaluation
  Board Pricing
The board used is the B-L475E-IOT01A Discovery kit that has a retail price of about 50€
Considering at least two rooms per section, the estimated cost will be around 500€
  Cloud Pricing
Azure Function: the first 400,000 GB/s of execution and 1,000,000 executions are free. Then you pay what you consume (serverless)
App service: The basic plan cost around 60€, for testing purpose we will use the free one.
Azure SQL Database: We choose to use the serverless option also in the DB, we use the maximum size of 15GB but it is possible to use more space.

## Slide 21: Pricing Evaluation

## Slide 22: To be done

## Slide 23: Evaluation for the last delivery
We have to test whether our cloud architecture is efficient enough for our purposes, our target remains to manage 20 devices per room.
  So we will perform a simulation, through a Python script, sending data to the cloud and analyzing the behavior of our algorithm, taking into account that saving data to the DB, from what we have experienced so far, is an important bottleneck
Evaluation of MQTT (we have to repeat a similar experiment using MQTT)

## Slide 24: Technical Evaluation
We will do a technical evaluation performing load tests on all parts of our system:
  BLE IoT device-Smartphone interaction: how many smartphones a single device can handle?
  Cloud IoT device-Cloud interaction: what is the message rate with which the device can send messages to Azure IoT hub?
  Responsiveness Cloud-Smartphone interaction: how fast the smartphone receives the advice on where to go, does it depend from the number of connected devices?

## Slide 25: User Experience Evaluation
We are planning evaluate the user experience using mockups, and after every demo of these prototypes we will collect people's opinions asking for feedbacks and publishing some google forms.
The questions will be mainly on:
  User interface
  Application services

## Slide 26: Thank you for listening